## Slide 1: SE 181 Introduction to Software Testing

## Slide 2: Defective Software
We develop programs that contain defects 
  How many? What kind?
Hard to predict the future, however… it is highly likely, that the software we (including you!) will develop in the future will not be significantly better.

## Slide 3: About Defective Software
Not all software defects result in “bad” things.
Some defects, however, result in “very bad” things.
Almost all defects have financial consequences.

## Slide 4: Some “Spectacular” Failures
NASA Mariner 1, Venus probe, Loss (1962)
  Period instead of comma in FORTRAN DO-Loop
Therac 25, Radiation overexposure, Loss of life (1985-1987)
  Very complex, inadequately tested system
AT&T Long Distance, Service failure for nine hours (1990)
  Wrong break statement in C-code
Pentium Processor, Division algorithm (1994)
  Incomplete entries in a look-up-table

## Slide 5: Some “Spectacular” Failures
Ariane 5, Explosion (1996)
  Data conversion of a too large number
USS Yorktown, Propulsion system shut down (1998)
  Input and division by ‘0’
Mars Climate Orbiter, Loss (1999)
  Mixture of pounds and Kilograms

## Slide 6: Many Reasons for Software Defects
Poor Requirements
  Poorly written, ambiguous, incorrect, and missing.
System Complexity
Poor programming
Inadequate testing
…
etc.

## Slide 7: SE Community Response
Improved environments for software development.
Better processes to ensure that we are building the right thing.
Technology to help us ensure that we built the thing right.

## Slide 8: Arsenal for Dependable Software
Automated development aids
Static source code analysis
Formal methods
  Requirements specification, Program Verification
Peer reviews
Testing

## Slide 9: The Significance of Testing
Most widely-used activity for ensuring that software systems satisfy the specified requirements.
Consumes substantial project resources. Some estimates: ~50% of development costs

## Slide 10: Limitations of Testing
Testing cannot occur until after the code is written.
The problem is big!
Perhaps the least understood major SE activity.
Exhaustive testing is not practical even for the simplest programs. WHY?
Even if we “exhaustively” test all execution paths of a program, we cannot guarantee its correctness  The best we can do is increase our confidence !
“Testing can show the presence of bugs, not their absence.” EWD

## Slide 11: Limitations of Testing
Testers do not have immunity to bugs.
Even the slightest modifications – after a program has been tested – invalidate (some or even all of) our previous testing efforts.
Automation is critically important, but costly and sometimes hard to implement.
Unfortunately, there are only a few good tools, and in general, effective use of these good tools is very limited.

## Slide 12: Some Terminology
Verification
  “Are we building the product right?”
  Does the software meet the specification?
Validation
  “Are we building the right product?”
  Does the software meet the user requirements?
Software Quality Assurance
  Not the same as software testing …
  Create and enforce standards and methods to improve the development process and to prevent bugs from occurring.

## Slide 13
Testing Strategy

## Slide 14: Testing Strategy
Divide-and-conquer !
We begin by “testing-in-the-small” and move toward “testing-in-the-large”
For conventional software
  The module (component) is our initial focus
  Integration of modules follows
For OO software
  Our focus when “testing in the small” changes from an individual module (the conventional view) to an OO class that encompasses attributes and operations and implies communication and collaboration

## Slide 15: Testing Strategy
Understand / formulate quality objectives
Identify the appropriate testing phases for the given release, and the types of testing need to be performed.
Prioritize the testing activities.
Plan how to deal with “cycles”

## Slide 16: Testing Phases
Unit Testing
Integration Testing
System Testing
Alpha Testing
Beta Testing
Acceptance Testing

## Slide 17: The V-Model

## Slide 18: Unit Testing
test cases
results
software
engineer
Module to be tested

## Slide 19: Unit Testing
Performed by each developer.
Scope: Ensure that each module (i.e., class, subprogram), or collection of modules as appropriate, has been implemented correctly.
“White-box” form of testing.

## Slide 20: Unit Testing
interface
local data structures
boundary conditions
error handling paths
module to
be tested
test cases

## Slide 21: Unit Test Environment
stub
stub
driver
RESULTS
interface
local data structures
boundary conditions
error handling paths
test cases

## Slide 22: Unit Testing
Need an effective adequacy criterion.
Work with sophisticated source-code analysis tools appropriate for the criterion and development environment.
May need to develop “stubs” and domain-specific automation tools.
Although a critical testing phase, it is often performed poorly ! WHY???

## Slide 23: Integration Testing

## Slide 24: Integration Testing
Performed by a small team.
Scope: Ensure that the interfaces between components (which developers could not test) have been implemented correctly.
Approaches:
  “big-bang”
  Incremental construction
Test cases have to be planned, documented, and reviewed.
Performed in a small time-frame

## Slide 25: Incremental vs. “Big-Bang”
Big-bang – Advantages:
  The whole system is available
Big-bang – Disadvantages:
  Hard to guarantee that all components will be ready at the same time
  Focus is not on a specific component
  Harder to locate errors
Incremental – Advantages:
  Focus is on each module  better testing ?
  Easy to locate errors
Incremental – Disadvantages:
  Need to develop special code (stubs and/or drivers)

## Slide 26: Top Down Integration
top module is tested with
stubs
stubs are replaced one at
a time, "depth first"
as new modules are integrated,
some subset of tests is re-run
A
B
C
D
E
F
G

## Slide 27: Bottom-Up Integration
drivers are replaced one at a
time, "depth first"
worker modules are grouped into
builds and integrated
A
B
C
D
E
F
G
cluster

## Slide 28: Sandwich Integration Testing
Top modules are
tested with stubs
Worker modules are grouped into
builds and integrated
A
B
C
D
E
F
G
cluster

## Slide 29: System Testing

## Slide 30: System Testing
Performed by a separate group within the organization. HOW LARGE ???
Scope: Pretend “we” are the end-users of the product.
Focus is on functionality, but must also perform many other types of tests (e.g., recovery, performance, etc.).
“Black-box” form of testing.
Test case specification driven by use-cases.

## Slide 31: System Testing
The whole effort has to be planned (System Test Plan).
Test cases have to be designed, documented, and reviewed.
Adequacy based on requirements coverage.
  but must think beyond stated requirements
Support tools have to be [developed]/used for preparing data, executing the test cases, analyzing the results.

## Slide 32: System Testing
Group members must develop expertise on specific system features / capabilities.
Often, need to collect and analyze project quality data.
End-user advocates but colleagues with the rest of the team…
The burden of proof is always on the ST group.
Often, the ST group gets the initial blame for “not seeing the problem before the customer did”.

## Slide 33: Other Testing Phases
Depending on the system being developed and the organization developing the system, other testing phases may be appropriate:
  Alpha / Beta Testing
  Acceptance Testing

## Slide 34: Types of Testing
Functionality
Performance
  Test the run-time performance of the software.
Stress
  Execute a system in a manner that demands resources in abnormal quantity, frequency, or volume.
Longevity / Reliability Testing
  Evaluate the behavior of the application when used for a long period of time under normal and peak load conditions. Estimate the likelihood that the requirements for failure rates, mean-time-between-failures, and so on, will be satisfied.

## Slide 35: Types of Testing
Recovery / Failover
  Force the software to fail in a variety of ways and verify that the recovery is properly performed.
Security
  Verify that protection mechanisms built into a system will, in fact, protect it from improper penetration.
Usability
  Attempt to identify discrepancies between the user interfaces of a product and the human engineering requirements of its potential users.
…

## Slide 36: Testing Phases vs. Types of Testing
It is very important to clearly understand the differences between Testing Phases and Types of Testing, and their relationships.

## Slide 37: Regression Testing
The activity of re-testing modified software.
It is common to introduce problems when modifying existing code to either correct an existing problem or otherwise enhance the program.
Options:
  Retest-none (of the test cases)
  Retest-all
  Selective retesting
For some systems, regression testing can be fairly expensive.

## Slide 38
Classification of Software Faults

## Slide 39: Bugs, Faults, Defects, and Glitches
"What's in a name? That which we call a bug by any other word would ..."
“A software bug is an error, flaw, mistake, failure, or fault in a computer program that prevents it from working as intended, or produces an incorrect result. Bugs arise from mistakes and errors, made by people, in either a program's source code or its design.” [wikipedia]
A fault results in a failure.

## Slide 40: The first “bug”
In 1947 Harvard University was operating a room-sized computer called the Mark II.
  mechanical relays
  glowing vacuum tubes
  technicians program the computer by reconfiguring it
  Technicians had to change the occasional vacuum tube.
A moth flew into the computer and was zapped by the high voltage when it landed on a relay.
Hence, the first computer bug!
  I am not making this up :-)

## Slide 41: Structural Bugs
Control and Sequence bugs
  Missing processing steps
  Duplicated | Unnecessary processing
  Improper nesting of loops
  Unreachable code
Logic bugs
  Improper negation of Boolean expressions
  Misunderstanding the semantics of the order in which Boolean expressions are evaluated for specific compilers (e.g., short circuits).
  Confusing OR with XOR
  “Impossible” cases that are not impossible
  “Don’t care” cases that matter

## Slide 42: Structural Bugs (cont’d)
Processing bugs
  Arithmetic bugs.
  Mathematical function evaluation.
  Algorithm selection.
  Conversion from one data representation to another.
  Ignoring overflow.
  Floating point number comparisons.
Initialization bugs
  Accepting an initial value without a validation check.
  Initializing to the wrong format, data representation, or type.
  A bug in the first value of a loop-control parameter.

## Slide 43: Data Bugs
Data bugs include all bugs that arise from the specification of data entities and their:
  format
  number
  initial values
Note:
Bugs in data are at least as common as bugs in code.
Data bugs account for more than 20% of all bugs in a typical software system!

## Slide 44: Implementation and Coding Bugs
Misunderstanding the semantics of operations and their potential side-effects.
Typographical bugs.
Standards violations.
Erroneous comments?

## Slide 45: Integration Bugs
Bugs having to do with the integration of presumably working and tested components.
External Interface Bugs
  Protocol errors and misunderstandings
  Invalid timing assumptions.
  Misunderstood input and output formats.
  Insufficient tolerance to bad input data.
Internal Interface Bugs
  Wrong subroutine call sequences
  Misunderstood call-parameters
  Misunderstood entry or exit parameter values

## Slide 46: Integration Bugs (cont’d)
Note:
Integration bugs are an expensive category because:
  they are caught late in the game
  they force changes in several components and/or data structures.

## Slide 47: System and Architecture Bugs
Bugs affecting the entire software system.
Usually, the result of incorrect assumptions about the system.
  there will be no interrupts
  that memory or registers are initialized ...
  little attention given to data backups
  not thinking about converting/priming the data base
  assuming that all I/O devices require the same control

## Slide 48: Observations About Fault Classification
The fault classification discussed here may not fit your project.
Consider having a classification scheme appropriate for your work/project/organization.
  IEEE 1044 provides a reasonable classification for faults.
It will help you better understand where the bugs come from.
Coming up with an effective classification of faults for any project requires an infrastructure and substantial amount of work!